## Slide 1: TRANSPORT TRAINING:
OXYGEN CALCULATION AND
TRANSPORT FORMS

## Slide 2
CONTENTS
OXYGEN USE
Oxygen therapy: Different O2 cylinders, Max. vol, max pressure, conversion factor
01
OXYGEN CALCULATION USING LOW-FLOW
Sample calculations
02
OXYGEN CALCULATION USING HIGH-FLOW
Sample calculations
03
ORIENTATION TO THE DIFFERENT TRANSPORT FORMS
Ambulance checklist, Equipment Checklist, Patient Transfer Form
04
Insert text here
Lorem ipsum dolor sit amet, simul adolescens ei vis, id nec errem interesset
05

## Slide 3
Oxygen Therapy During Transport: How to Calculate Oxygen Needs

## Slide 4: Commonly used oxygen cylinders
The most commonly used oxygen cylinders in the Royal Hospital are D and E.
Size of Cylinder | Maximum pressure | Maximum volume | Conversion factor
D | 2216 | 356 | 0.16
E | 2216 | 625 | 0.28
Conversion factor is calculated by dividing the maximum volume by the maximum pressure

## Slide 5: Cylinder Duration Chart in Minutes

## Slide 6: Oxygen Cylinder Duration Calculation: LOW FLOW
Low flow oxygen source:
cylinder pressure (psi) x cylinder factor
Duration of flow (minute) =
oxygen flow (Liters/min)
Example: a 1 year old child on nasal prongs at 2L/min
2000 psi x 0.28 280min (to convert to hours)
2L/min
280min/ 60minutes = 4.6 hours
E Cylinder
Conversion factor: 0.28

## Slide 7: How To Calculate Oxygen During Transfer?
First Step: Calculate patient’s oxygen consumption
> Spontaneously breathing patient on oxygen:
1. Check flow rate e.g 2L/min
2. Check total journey including moving from the ward to ambulance, loading time, travel, unloading
and moving from ambulance to the ward e.g 60 minutes
3. Calculate oxygen consumption. Multiply oxygen flow rate into total duration of journey in minutes
e.g 2L/min x 60 minutes = 120 minutes
4. DOUBLE total oxygen consumption. e.g 120 minutes x 2 = 240 minutes
5. Convert minutes into hours ( 1hour=60minutes)
e.g 240 minutes/60min = 4 hours. You need oxygen that will last for 4 hours
> Ventilated patients: (LOW FLOW OXYGEN SOURCE)
1. Use oxygen calculation charts for E and D cylinders to calculate oxygen consumption based on
oxygen flow rate on the ventilator
2. Check oxygen capacity in the cylinder
3. Double oxygen consumption
Second Step:
1. Check the type of cylinder: either D or E
2. Check the pressure of the cylinder
3. Use oxygen calculation charts for D and E cylinders to check capacity

## Slide 8: SCENARIO # 1
You have a 5-year old child who is scheduled for CT. He is on oxygen at 3L/min via nasal cannula. The entire procedure is expected to last for 30 minutes.
Calculate the child’s oxygen consumption throughout the process
Demonstrate how to check the capacity of the cylinder

## Slide 9: SCENARIO # 2
You were informed to transfer a patient to Sur Hospital. The patient is on 8L/min of oxygen. How many cylinders of oxygen will you need during the trip.

## Slide 10: SCENARIO # 3
A 5-month old child is scheduled for ENT assessment to Al Nahda. He is currently on nasal prongs at a rate of 1L/min. On the way back, the child is ventilated on a transport ventilator which uses 1L/min on
following settings: PIP 20 PEEP 7 Rate 30/min
Calculate the child’s oxygen consumption throughout the trip (considering entire process will be total
of 4 hours)
2. Demonstrate how to check the capacity of the cylinder

## Slide 11: How To Calculate Oxygen During Transfer?
> Ventilated patients: (HIGH FLOW OXYGEN SOURCE)
1. Use the formula:
(expiratory minute vol in L + baseflow(3L/min) + minute ventilation leak) X (set FiO2-20.9) / 79.1 x transport
duration in minutes
2. Double the oxygen consumption
Second Step:
1. Check the type of cylinder: either D or E
2. Check the pressure of the cylinder
3. Use oxygen calculation charts for D and E cylinders to check capacity

## Slide 12: Example:
Expiratory minute volume 5L
Total MV leakage 1L/min
Base flow 3L/min
Set FiO2 50%
Planned duration of transport 120mins
Formula: (MV + BF + MV leak) X (FiO2-20.9) / 79.1 X transport duration
(5L + 3L + 1L) x (50%-20.9) / 79.1 X 120mins
9 x 29.1
= 3.3L/min X 120mins = 396 Liters
79.1
The full E cylinder estimated volume is 625 so with above parameters and planned time, this is enough but, it is safer to have an extra cylinder as standby.

## Slide 13: Scenario 1:
You are involved in the transfer of a 2-year old child from Royal Hospital A&E to Nizwa Hospital.
He is ventilated on a portable ventilator that uses high pressure oxygen source.
He is ventilated on Tidal volume 200ml, Rate 25/min FiO2 50%, minute ventilation = 5000ml. There is no leak. Expected trip would last for 3 hours (180minutes)
Calculate oxygen requirement.
Formula: (MV + BF + MV leak) X (FiO2-20.9) / 79.1 X transport duration
Expiratory minute volume 5L
Total MV leakage 0L/min
Base flow 3L/min
Set FiO2 50%
Planned duration of transport 3 HOURS
Formula: (MV + BF + MV leak) X (FiO2-20.9) / 79.1 X transport duration
(5L + 3L + 0L) x (50%-20.9) / 79.1 X 120mins
8 x 29.1
= 2.9L/min X 180mins = 529.75 Liters
79.1

## Slide 14
INTRODUCTION TO TRANSPORT FORMS

## Slide 15: AMBULANCE CHECKLIST
Oxygen Therapy During Transport: How to Calculate Oxygen Needs Oxygen Therapy During Transport: How to Calculate Oxygen Needs

## Slide 16: AMBULANCE CHECKLIST (cont.)

## Slide 17: TRANSPORT CHECKLIST

## Slide 18: TRANSPORT CHECKLIST

## Slide 19: PATIENT TRANSFER FORM

## Slide 20: PATIENT TRANSFER FORM (cont.)
TO BE FILLED OUT BY THE DOCTOR

## Slide 21: THANK YOU